## Slide 1: Reconstructing meteoroid trajectories using simulated data
Joachim Balis
Supervisors:
Hervé Lamy (Royal Belgian Institute for Space Aeronomy)
Emmanuel Jehin (Origins in Cosmology and Astrophysics, ULiège)

## Slide 2: Adapted from Hervé Lamy’s IMC 2021 presentation
Set of  6 non-linear equations which contains the time delays ti between appearances of meteor echoes at station i and a reference station.
Non-linear solver + additional constraints on height of the specular reflection point (e.g. between 85 and 110 km) and speed values (≥ 11 km/s and ≤ 72 km/s)
Specular reflection : Si = RTi + RRi must be minimum for each station i
6 unknowns: 3 coordinates of one specular point P0 + 3 components of speed v (assumed to be constant)
At least 6 equations : dSi / dt = 0 i=1, …, n
Distance minimization
! Here the time delays are not obtained by measurements. They are computed theoretically and are then injected into the system of n equations !

## Slide 3: Equations nondimensionalization
Dimensions: Distance/Time
Dimensionless
Solution vector
Specular point for station j
Location of station j

## Slide 4: Solver
lsqnonlin
fmincon
Find minimum of constrained nonlinear multivariable function
Allows the introduction of (in)equality linear and nonlinear constraints
Solve nonlinear least-squares (nonlinear data-fitting) problems
Does not allow the introduction of constraints
The target objective (to be minimized) has to be scalar: chosen initially as the L2-norm of the n equations dSi / dt = 0

## Slide 5: Trajectory 105
Theoretical solution (from CAMS)
Echo theoretically detected by 16 stations but only 7 are exploited from the BRAMS data
Reconstructed solution

## Slide 6: Convergence map Vx-Vy – Default Guess
Default Guess
Actual solution

## Slide 7: Smoothness maps
Variation of the objective function with X0 and Y0 (other parameters are converged)
Valley with multiple critical points
Correct solution
Solver can fall there and never recover..

## Slide 8: Towards a better target objective...
Here we have two weighted terms:
  The first one penalizes the solver if it finds a trajectory which does not minimize the total distance travelled by the signal (from the transmitter to the receptor after reflection at the specular point).
  The second one penalizes the solver if the time delays reconstructed from the solution are different from the observed time delays.
The only disadvantage is that it takes about 5-7x more computational time.
From now on, we will set w1 = 0:

## Slide 9: Trajectory 105
Theoretical solution (from CAMS)
Reconstructed solution

## Slide 10: Convergence map Vx-Vy – Default Guess
Default Guess
Actual solution

## Slide 11: Smoothness maps
Variation of the objective function with X0 and Y0 (other parameters are converged)
Solver could still be stuck here
Correct solution

## Slide 12: Uncertainty on the trajectory 105
Number of stations - weights | Noise [ms] | Error on the trajectory angle [°] | Error on the trajectory position [km] | Error on the velocity norm [km/s]
7 – w1 = 1, w2 = 0 | 0 (theoretical) | 0,064 | 2,901 | 0,104
7 – w1 = 0, w2 = 1 | 0 (theoretical) | 0,0009 | 0,002 | 0,0002
7 – w1 = 1, w2 = 0 | 2 | 9,43 | 56,49 | 4,23
7 – w1 = 0, w2 = 1 | 2 | 1,12 | 9,20 | 0,58
7 – w1 = 1, w2 = 0 | 5 | 18,43 | 99,49 | 7,23
7 – w1 = 0, w2 = 1 | 5 | 6,83 | 22,65 | 0,79
9 – w1 = 1, w2 = 0 | 5 | 7,81 | 25,01 | 4,12
9 – w1 = 0, w2 = 1 | 5 | 0,51 | 11,39 | 0,53
9 – w1 = 1, w2 = 0 | 10 | 15,12 | 75,13 | 6,42
9 – w1 = 0, w2 = 1 | 10 | 5,42 | 24,12 | 3,28
We analyze the effect of errors on the input time delays on the output trajectory
To do so, we add some random noise on the measurements of the time delays around the correct theoretical value

## Slide 13: Trajectory 105 reconstructed with 5E-3 error

## Slide 14: Uncertainty on the trajectory 105
The maximum error is of the order of 60 ms, far too much for our algorithms to converge
With 7 stations, 5 ms is too much uncertainty even with the added terms
With 9 stations, 5 ms is handled well with the novel target while it diverges with the old target => important improvement
Need for a better post-processing (substraction of the direct signal, filtering) at the receiving stations

## Slide 15: Post-processing steps
The signal is acquired at the station with a sampling frequency of 5512 Hz and is then centered around 1000Hz.
The direct beacon signal is reconstructed and subtracted.
A window of 10 seconds around the theoretical appearance time of the signal is selected and a Blackman filter is applied.
The envelope of the filtered signal is obtained through an Hilbert transform.
The half-rise time is identified on the envelope signal.

## Slide 16
The clock which gives an error of about 1ms for Windows stations and 0.166 ms for Raspberry Pi stations.
The electronics circuitry at the stations: analogue filters introduce delays.
The wave propagation delay: the maximum difference of distance travelled by the wave between two stations is of the order of 100km, i.e. 0.33 ms of potential error.
The main error source comes from the selection of the half-rise time on the WAV files.
Sources of experimental errors
Arbitrary power unit
Time [s]
Power of the filtered envelope signal for NLMAAS

## Slide 17
Bilzen spectrogram
Zoom on the meteor echo of Bilzen spectrogram

## Slide 18
Low-pass Blackman: 1050 Hz
High-pass Blackman: 1000 Hz
Rise time of 0.06s
D
D
D
Low-pass Blackman: 1022 Hz
High-pass Blackman: 1007 Hz
Rise time of 0.10s

## Slide 19
Reconstructed solution
Trajectory 105 reconstructed with best experimental time delays
Error on the trajectory position = 59,52 km
Error on the trajectory angle = 16,27°
Error on the velocity norm = 1,07 km/s

## Slide 20: Conclusions & Perspectives
The solver has been corrected, adapted and improved.
The signal post-processing needs to be improved (subtraction of the direct signal and noise filtering).
There is a trade-off between a fast rise time and enough filtering.
Currently, it seems difficult to obtain the required accuracy of < 5 ms.
Simulated meteors will be used to quantify the filtering impact on the signal rise.

## Slide 21: Thank you for your attention!

## Slide 22: Appendices

## Slide 23: Convergence criteria

## Slide 24: Convergence criteria

## Slide 25
Simulation of a meteor signal modulated by a sine wave at 1000Hz and bandpass filtered
+-10 Hz filter

## Slide 26: Analysis of the Blackman filter impact
+-50 Hz filter
+-10 Hz filter

## Slide 27: Analysis of the Blackman filter impact
+-5 Hz filter
+-2 Hz filter

## Slide 28
Simulation of a meteor signal modulated by a combili of sine waves at different frequencies & modulated in amplitude by a Gaussian
with

## Slide 29
Simulation of a meteor signal modulated by a combili of sine waves at different frequencies & modulated in amplitude by a Gaussian
Here the carrier is a combili of sine waves between 998 and 1002 Hz (by step of 0.067Hz) and modulated by the same Gaussian as before
We only have non-zero coefficients between 998 and 1002 Hz